## Slide 1: Presentation II on Unicycle and Differential Drive WMR EE 555 – Automation Lab
By- Meesala Ganesh
Narendra Sona
Santanu Barat
UNDER THE GUIDANCE OF Dr. Parijat Bhowmick

## Slide 2: INTRODUCTION
Robots
Machines programmable by a computer
capable of carrying out complex series of actions
Mobile Robots
Locomotion Property
Mobile Robot. Source: Katte 2018.

## Slide 3
WHEELED MOBILE ROBOT
Features :
Locomotion
Consume less energy and move faster
Less stability problems
Source: www.automaticaddison.com
Types:
Unicycle
Differential drive WMR
Tricycle WMR
Car-like WMR

## Slide 4: Turtlebot Specifications
Maximum linear velocity – 0.22m/sec
Maximum rotational velocity- 2.84 rad/sec
Weight- 1 kg
SBC(Single Board Computer)- Raspberry pi
A single-board computer (SBC) is a complete computer built on a single circuit board, with microprocessor(s), memory, input/output (I/O) and other features required of a functional computer.
MCU-32-bit ARM Cortex®-M7
The arm cortex-M7 processor is the highest performing processor in cortex –M family that enables the design of sophisticated MCUs.

## Slide 5
Actuator-XL430-W250 (servo)
It is a cored motor with control modes of position and velocity.
DYNAMIXEL is an intelligent robot-exclusive actuator with a fully integrated DC motor + reduction gearbox + controller + pilot + network in a DC servo module.
LDS(Laser Distance Sensor)
360 Laser Distance Sensor LDS-01 is a 2D laser scanner capable of sensing 360 degrees that collects a set of data around the robot to use for SLAM (Simultaneous Localization and Mapping) and Navigation.
Battery-Lithium polymer 11.1V 1800mAh / 19.98Wh 5C
Power Adaptor
Input: 100-240V, AC 50/60Hz, 1.5A @max
Output: 12V DC, 5A
Power Connectors
Status LED
Buttons and Switches

## Slide 6
UNICYCLE WMR:
Unicycle is a conventional wheel rolling on a horizontal plane, while keeping its body vertical
Kinematics are as follows -
Here, v is the linear velocity and is the angular
velocity
Input: v and
Output : x,y and theta
0
X
Y
Fig.1 : Kinematic Model of Unicycle

## Slide 7
Differential Drive WMR :
A wheeled mobile robot whose movement is based on two separately drive wheels placed on either side of the robot body.
Kinematics are as follows -
Here, = change in position of the robot in x direction
= change in position of the robot in y direction
= change in orientation angle of the robot
= radius of each wheel of the robot
= separation between the two wheels
X
Y
0
q
Fig.2 : Kinematic Model of Differential Drive WMR

## Slide 8
We know that
So, the above equations becomes
Here, = velocity of the right wheel
= velocity of the left wheel
=
In matrix form ,
TRANSFORMATION MATRIX
Helpful in writing these equations

## Slide 9
SIMULINK MODEL of UNICYCLE :

## Slide 10
Result : X-Y Position using XY Graph Block of Simulink Model

## Slide 11
SIMULINK MODEL of DIFFERENTIAL DRIVE WMR :
PID Controller

## Slide 14
Result and Analysis: Trajectory tracking of final PID Controller

## Slide 15
Linear velocity along x and y directions

## Slide 16
Angular velocity

## Slide 17
Experimental Validation :
Open Loop:
Gazebo simulation:

## Slide 18
Turtlebot implementation:

## Slide 19
Conclusion:
In this lab we learned and implemented both open loop and closed loop simulink models of unicycle and differential drive 2- wheeled mobile robots.
Designed PID controller for achieving a rectangular trajectory tracking and verified the open loop simulation results with Gazebo simulation and experimental validation using turtlebot.
Future Works:
This work can be extended for complex trajectory tracking and obstacle avoidance problems.
Further, it can be used for controlling of multiagent mobile robots.

## Slide 20
Thank you